## Slide 1: Identifying the Lattice Parameters
(In your groups) determine the lattice vectors and basis for the smallest possible unit cell (more than one possible answer)
If you finish, draw the lattice.

## Slide 2: Identifying the Lattice Parameters
(In your groups) determine the lattice vectors and basis for the smallest possible unit cell (more than one possible answer)
If you finish, draw the lattice.

## Slide 3: Identifying the Lattice Parameters
a) Situation of atoms at the corners of regular hexagons
(In your groups) determine the lattice vectors and basis for the smallest possible unit cell (more than one possible answer)
If you finish, draw the lattice.

## Slide 4: Identifying the Lattice Parameters
α
a1
a2
O
y
x
b) Crystal lattice obtained by identifying all the lattice points in (a)
a) Situation of atoms at the corners of regular hexagons
(In your groups) determine the lattice vectors and basis for the smallest possible unit cell (more than one possible answer)
If you finish, draw the lattice.

## Slide 5: Bravais Lattices in 2D
In 2D there are five ways to order atoms in a lattice
Special case where angles go to 90
a=b
Special case where point halfway
a=b
parallelogram
Notes: More common to use non-primitive in 3d (next slide)

## Slide 6: Bravais Lattices in 2D A Bravais lattice looks the same from any lattice point.
In 2D there are five ways to order atoms in a lattice
Primitive unit cell: contains only one lattice point (but 4 points?)
Are the dotted lattices primitive?
  Non-primitive unit cells sometimes useful if orthogonal coordinate system can be used
Special case where angles go to 90
a=b
Special case where point halfway
a=b
parallelogram
Notes: More common to use non-primitive in 3d (next slide)

## Slide 7: Why can't the blue triangle be a unit cell?
Not primitive
Notes: When it translates, it has to cover all space in the crystal. There are three axes here; you can’t even pick two vectors.

## Slide 8: Defining a lattice means writing lattice vectors
A Bravais lattice is a set of points such that a translation from any point in the lattice by a vector;
R = u1 a1 + u2 a2
locates an exactly equivalent point, i.e. a point with the same environment. This is translational symmetry.
1. It should cover the whole space.
2. In 2D, there should be only 2 vectors.
What would they be here?

## Slide 9: You can define a vector by its lattice points. (More on this later.)
Not primitive
A Bravais lattice is a set of points such that a translation from any point in the lattice by a vector;
R = u1 a1 + u2 a2
locates an exactly equivalent point, i.e. a point with the same environment.
If the start of the vector is at (0,0), what lattice point would this be?
(0,0)
Notes: When it translates, it has to cover all space in the crystal. There are three axes here; you can’t even pick two vectors.

## Slide 10
Lattice Vectors – 3D
A three dimensional crystal is described by 3 fundamental translation vectors a, b and c (AKA: a1, a2 and a3)
r = u1 a + u2 b + u3 c
Also common:
R = h a1 + k a2 + l a3
Sometimes people will use [h k l] instead of u’s.
(more common to see in reciprocal space, later)
Notes: Again, calling stuff by different names can be very confusing, particularly in this field.
Kittel uses a1, a2 and a3

## Slide 11: Solid Models: Close-Packed Spheres
Many atoms or ions forming solids have spherical symmetry (e.g. noble gases and simple metals)
Considering the atoms or ions as solid spheres we can imagine crystals as closely packed spheres
How can we pack them?

## Slide 12: Simple cubic
The simple cubic structure is a Bravais lattice.
How many lattice points are in each unit cell?
a
b
c
R = u1 a + u2 b + u3 c
Notes: Bravais lattice means that when you move along any lattice vectors, the resulting symmetry/environment is exactly the same

## Slide 13: Simple cubic
We can also simply count the lattice points we see in one unit cell.
But we have to keep track of how many unit cells share these atoms.
1/8 atom
1/8 atom
1/8 atom
1/8 atom
1/8 atom
1/8 atom
1/8 atom
1/8 atom
Notes: another way of viewing this: count all the atoms in the unit cell
keep track of atom sharing!
also gives one atom
easier: construct cubic box around one atom!

## Slide 14: ATOMIC PACKING FACTOR (APF)
a

## Slide 15: ATOMIC PACKING FACTOR (APF)
contains 8 x 1/8 =
1
atom/unit cell
Lattice constant
close-packed directions (where they touch)
a
R=0.5a

## Slide 16: ATOMIC PACKING FACTOR (APF)
contains 8 x 1/8 =
1
atom/unit cell
Lattice constant
close-packed directions (where they touch)
a
R=0.5a

## Slide 17: ATOMIC PACKING FACTOR (APF)
APF for the simple cubic structure = 0.52
contains 8 x 1/8 =
1
atom/unit cell
Lattice constant
close-packed directions (where they touch)
a
R=0.5a

## Slide 18: Simple cubic
A simple cubic structure is not efficient at packing spheres (atoms occupy only 52% of the total volume). Marbles will not resemble.
Only one single element crystallizes in the simple cubic structure (polonium). More multi-elements.
Notes: If we took a bunch of marbles, we wouldn’t expect to see them stack this way.
Po is a rare metal

## Slide 19: How Else Can We Stack
How else might be a way to stack up these marbles that represent atoms?
Notes: Hard to keep cubic. Too easier tilted. Compare to triangular lattice.

## Slide 20: How Else Can We Stack
How else might be a way to stack up these marbles that represent atoms?
Often drawn as different colors (for easy viewing) but these are NOT different atoms!
Notes: Hard to keep cubic. Too easier tilted. Compare to triangular lattice.

## Slide 21: How Else Can We Stack
How else might be a way to stack up these marbles that represent atoms?
Often drawn as different colors (for easy viewing) but these are NOT different atoms!
Notes: Hard to keep cubic. Too easier tilted. Compare to triangular lattice.

## Slide 22: Let’s count the number of atoms
Vertex(corner) atom shared by 8 cells Þ 1/8 atom per cell
Notes: In groups: Discuss # of atoms per cell
These are all lattice points and the definition of a lattice point is that the environment has to be the same as all other lattice points.
IF THEY WERE DIFFERENT ATOMS, THIS WOULD NOT BE THE SAME STRUCTURE.

## Slide 23: # of Lattice points/Unit Cell
Face Centered Cubic (FCC)

## Slide 24: # of Lattice points/Unit Cell
For atoms in a cubic unit cell:
Points on faces are ½ within the cell
Points on Faces
Face Centered Cubic (FCC)

## Slide 25: # of Lattice points/Unit Cell
For atoms in a cubic unit cell:
Points on faces are ½ within the cell
How many full atoms are in this cube?
Face Centered Cubic (FCC)

## Slide 26: Three Cubic Unit Cell Types in 3D
Vertex(corner) atom shared by 8 cells Þ 1/8 atom per cell
Edge atom shared by 4 cells Þ 1/4 atom per cell
Face atom shared by 2 cells Þ 1/2 atom per cell
Body unique to 1 cell Þ 1 atom per cell
Notes: Discuss/draw edge and unit cells to help visualize (draw on sc for simplicity)
In groups: Discuss # of atoms per cell

## Slide 27: Three Cubic Unit Cell Types in 3D
Vertex(corner) atom shared by 8 cells Þ 1/8 atom per cell
Edge atom shared by 4 cells Þ 1/4 atom per cell
Face atom shared by 2 cells Þ 1/2 atom per cell
Body unique to 1 cell Þ 1 atom per cell
Are these primitive unit cells?
Notes: In groups: Discuss # of atoms per cell

## Slide 28
UNIT CELLS
Primitive
Single lattice point per cell
Smallest area in 2D, or
Smallest volume in 3D
Simple cubic(sc)
Conventional = Primitive cell
Notes: Common to get confused and think there should be only one atom per unit cell, but there can be multiple atoms in a basis!

## Slide 29
UNIT CELLS
Primitive
Conventional & Non-primitive
Single lattice point per cell
Smallest area in 2D, or
Smallest volume in 3D
More than one lattice point per cell
Integral multiples of the
area/volume of primitive cell
Body centered cubic(bcc)
Conventional ≠ Primitive cell
Simple cubic(sc)
Conventional = Primitive cell
Notes: Common to get confused and think there should be only one atom per unit cell, but there can be multiple atoms in a basis!

## Slide 30
UNIT CELLS
Primitive
Conventional & Non-primitive
Single lattice point per cell
Smallest area in 2D, or
Smallest volume in 3D
More than one lattice point per cell
Integral multiples of the
area/volume of primitive cell
Body centered cubic(bcc)
Conventional ≠ Primitive cell
Simple cubic(sc)
Conventional = Primitive cell
Notes: Common to get confused and think there should be only one atom per unit cell, but there can be multiple atoms in a basis!

## Slide 31: BODY CENTERED CUBIC STRUCTURE (BCC)
What is the close packed direction?
--Note: All atoms are identical; the center atom is shaded differently only for ease of viewing.
a
Notes: Along the diagonal

## Slide 32: BODY CENTERED CUBIC STRUCTURE (BCC)
What is the close packed direction?
What kind of adjustments would we make to calculate the atomic packing factor?
a
APF for simple cubic:
Notes: Along the diagonal

## Slide 33: Better packing than SC
In the body-centred cubic (bcc) structure 68% of the total volume is occupied.
Next-nearest neighbors relatively close by – make structure stable in some instances. Examples: Group I metals, Ba, V, Nb, Ta, W, Mo, Cr, Fe
Is this cube a primitive lattice?
Notes: How would you select a primitive unit cell? What volume should it have? (half of the conventional as there are 2 atoms in the conventional cubic cell). Select primitive lattice vectors along the body diagonals (they will not be orthogonal).
Easy to see why easier to use orthogonal convention lattice.

## Slide 34: Better packing than SC
In the body-centred cubic (bcc) structure 68% of the total volume is occupied.
Next-nearest neighbors relatively close by – make structure stable in some instances. Examples: Group I metals, Ba, V, Nb, Ta, W, Mo, Cr, Fe
Is this cube a primitive lattice?
No. The bcc structure is a Bravais lattice but the edges of the cube are not the primitive lattice vectors. Not smallest Vol.
Notes: How would you select a primitive unit cell? What volume should it have? (half of the conventional as there are 2 atoms in the conventional cubic cell). Select primitive lattice vectors along the body diagonals (they will not be orthogonal).
Easy to see why easier to use orthogonal convention lattice.

## Slide 35: Better packing than SC
How does the volume of the bcc primitive cell compare to the volume of the conventional cell?
Notes: It is half the volume

## Slide 36: FACE CENTERED CUBIC STRUCTURE (FCC)
Note: All atoms are identical; the face-centered atoms are shaded differently only for ease of viewing.
What is the close packed direction?

## Slide 37: FACE CENTERED CUBIC STRUCTURE (FCC)
Note: All atoms are identical; the face-centered atoms are shaded differently only for ease of viewing.
What are the lattice directions of the primitive unit cell?

## Slide 38: Simple Crystal FCC
Another view
Notes: Part of 2V2

## Slide 39: Simple Crystal FCC
Another view
Notes: Part of 2V2

## Slide 40: Simple Crystal FCC
Another view
How does the volume of the fcc primitive cell compare to the volume of the conventional cell?
Notes: Part of 2V2

## Slide 41: Groups: Fill in this Table for Cubic Structures
 | SC | BCC | FCC
Volume of conventional cell | a3 | a3 | a3
# of atoms per cubic cell | 1 | 2 | 4
Volume, primitive cell | a3 | ½ a3 | ¼ a3
# of nearest neighbors | 6 | 8 | 12
Nearest-neighbor distance | a | ½ a 3 | a/2
# of second neighbors | 12 | 6 | 6
Second neighbor distance | a2 | a | a
Notes: If running low on time, only have them figure out number of nearest neighbors
While they still have their magnetic blocks
Mention that # NN=coordination number

## Slide 42: Groups: Fill in this Table for Cubic Structures
 | SC | BCC | FCC
Volume of conventional cell | a3 | a3 | a3
# of atoms per cubic cell | 1 | 2 | 4
Volume, primitive cell | a3 | ½ a3 | ¼ a3
# of nearest neighbors | 6 | 8 | 12
Nearest-neighbor distance | a | ½ a 3 | a/2
# of second neighbors | 12 | 6 | 6
Second neighbor distance | a2 | a | a
Notes: If running low on time, only have them figure out number of nearest neighbors
While they still have their magnetic blocks
Mention that # NN=coordination number

## Slide 43
8
Coordination number
6
Primitive cubic
Body centered cubic
Face centered cubic
12

## Slide 44: Groups: Fill in this Table for Cubic Structures
 | SC | BCC | FCC
Volume of conventional cell | a3 | a3 | a3
# of atoms per cubic cell | 1 | 2 | 4
Volume, primitive cell | a3 | ½ a3 | ¼ a3
# of nearest neighbors | 6 | 8 | 12
Nearest-neighbor distance | a | ½ a 3 | a/2
# of second neighbors | 12 | 6 | 6
Second neighbor distance | a2 | a | a
Notes: If running low on time, only have them figure out number of nearest neighbors
While they still have their magnetic blocks
Mention that # NN=coordination number