## Slide 1: Objectives Critical for Future
Before we move on to more complex crystal structures, students should learn how to:
Draw Wigner-Seitz cell for a 2D lattice and be able to identify the number of sides (along what directions) for 3D
Address why we care about planes/directions
Correctly use/identify notation for directions and planes
Locate directions and planes
Determine the distance between planes in cubic or orthorhombic (abc, 90 angles) lattices
Notes: Consider bringing large crystal structure to show direction in real 3D

## Slide 2: Show me some ways that you could define a unit cell for this lattice.
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 3: There are many ways to define a unit cell. Here is one that will seem weird now, but will become important later.
1. Pick a center atom (origin) within the lattice
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 4
1. Pick a center atom (origin) within the lattice
2. Identify nearest neighbors (1st,2nd, 3rd to be safe)
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 5
1. Pick a center atom (origin) within the lattice
2. Draw perp. bisector to all neighbors (1st,2nd, 3rd to be safe)
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 6
1. Pick a center atom (origin) within the lattice
2. Draw perp. bisector to all neighbors (1st,2nd, 3rd to be safe)
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 7: Wigner-Seitz Method for Defining a Primitive Unit Cell (still applies in 3D)
1. Pick a center atom (origin) within the lattice
2. Draw perp. bisector to all neighbors (1st,2nd, 3rd to be safe)
3. Draw smallest polyhedron enclosed by bisectors
Always 6 sided in 2D, unless the lattice is rectangular.
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 8: Wigner-Seitz Method for Defining a Primitive Unit Cell (still applies in 3D)
1. Pick a center atom (origin) within the lattice
2. Draw perp. bisector to all neighbors (1st,2nd, 3rd to be safe)
3. Draw smallest polyhedron enclosed by bisectors
This is NOT the Brillouin Zone. But, it will be related to something we call the first Brillouin zone soon!
Notes: Have students come up with colored chalk and show different definitions of the unit cell to emphasize why it’s nice to have a specific definition. The Wigner-Seitz method will have an even more important use when we get to reciprocal space.
Reference to neighbors, like we discussed for sc, bcc and fcc
Sometimes don’t need to go to 3rd neighbors; it depends on the symmetry of the lattice. Best just to check though.

## Slide 9
Group: Create Wigner-Seitz cell of the graphene lattice
Notes: It’s ok if we don’t get to this as we’ll do a similar one in the BZ lecture.

## Slide 10
Group: Create Wigner-Seitz cell of the graphene lattice
Notes: It’s ok if we don’t get to this as we’ll do a similar one in the BZ lecture.

## Slide 11: Determine the Wigner-Seitz cell for a simple cubic lattice
a
Notes: Do we see an effect from the second nearest neighbors for this structure? Not this time, but we will in other cubic lattices (see next slide).

## Slide 12: Wigner-Seitz 3D cells For now, just a specific way to make up a unit cell.
Looks a little different in FCC. Why?
Is this BCC or FCC?
How many sides does each have?
 | BCC | FCC
# of nearest neighbors | 8 | 12
# of second neighbors | 6 | 6
Do these look familiar?
Notes: Answer: Not atom in the center of the cell.
Notice FCC only has 12, the second nearest neighbor is too far away.
Familiar? Probably should be. We will relate these to the Brillouin Zone soon, but we aren’t quite ready for that yet.

## Slide 13: Crystal Direction Notation
Figure shows
[111] direction
Choose one lattice point on the line as an origin (point O). Choice of origin is completely arbitrary, since every lattice point is identical.
Then choose the lattice vector joining O to any point on the line, say point T. This vector can be written as;
R = n1 a1 + n2 a2 + n3 a3
a1, a2, a3 often written as a, b, c or even x, y, z
To distinguish a lattice direction from a lattice point (x,y,z), the triplet is enclosed in square brackets and use no comas. Example: [n1n2n3]
[n1n2n3] is the smallest integer of the same relative ratios. Example: [222] would not be used instead of [111].
Negative directions can be written as
Also sometimes [-1-1-1] (nonideal)
Point T = (1,1,1)
Notes: Draw regular lattice on the board. Discuss how could pick any point on lattice as origin. Draw a vector through a few points. Maybe up and to right through.

## Slide 14: Group: Determine the crystal directions
X = -1 , Y = -1 , Z = 0 [110]
X = 1 , Y = 0 , Z = 0 [1 0 0]
X = 1 , Y = ½ , Z = 0
[1 ½ 0] [2 1 0]
X = ½ , Y = ½ , Z = 1
[½ ½ 1] [1 1 2]
[210]

## Slide 15: Group: Determine the Crystal Direction
X =-1 , Y = 1 , Z = -1/6
[-1 1 -1/6] [6 6 1]
We can move vectors to the origin as long as don’t change direction or magnitude.
Now let’s do one that’s a little harder.

## Slide 16: Crystal Planes
Within a crystal lattice it is possible to identify sets of equally spaced parallel planes, called lattice planes.
The density of lattice points on each plane of a given set is the same (due to translational symmetry).
b
a
b
a
A couple sets of
planes in the same
2D lattice.

## Slide 17: Why are planes in a lattice important?
(A) Determining crystal structure
* Diffraction methods measure the distance between parallel lattice planes of atoms to determine the lattice parameters (and other stuff)
(B) Plastic deformation
* Plastic deformation in metals occurs by the slip of atoms past each other.
* This slip tends to occur preferentially along specific crystal-dependent planes.
(C) Transport Properties
* In certain materials, atomic structure in some planes causes the transport of electrons and/or heat to be particularly rapid in some planes, and relatively slow in other planes.
• Example: Graphite: heat conduction is strong within the graphene sheets.

## Slide 18: Miller Indices (h k l ) for plane notation (no comas)
Miller Indices represent the orientation of a plane in a crystal and are defined as the reciprocals of the fractional intercepts which the plane makes with the crystallographic axes.
To determine Miller indices of a plane, take the following steps:
1) Determine the intercepts of the plane along each of the three crystallographic directions
2) Take the reciprocals of the intercepts
3) If fractions result, multiply each by the denominator of the smallest fraction
(multiply again if needed to get smallest possible ratio)
Notes: 3) Example: Let’s say your intercepts were 2, 3 and 1. Then the reciprocals would be: (1/2 1/3 1), multiply by 3 as 1/3 is the smallest fraction. Then would have to multiply again by 2.

## Slide 19: Example-1
Axis | X | Y | Z
Intercept points | 1 | ∞ | ∞
Reciprocals | 1/1 | 1/ ∞ | 1/ ∞
Smallest Ratio | 1 | 0 | 0
Miller İndices (100) |  |  | 
1) Determine the intercepts directions
2) Take the reciprocals of the intercepts
3) If fractions result, multiply
(1,0,0)

## Slide 20
Axis | X | Y | Z
Intercept points | 1 | 1 | ∞
Reciprocals | 1/1 | 1/1 | 1/ ∞
Smallest Ratio | 1 | 1 | 0
Miller İndices (110) |  |  | 
Example-2
(1,0,0)
(0,1,0)
1) Determine the intercepts directions
2) Take the reciprocals of the intercepts
3) If fractions result, multiply

## Slide 21
Axis | X | Y | Z
Intercept points | 1 | 1 | 1
Reciprocals | 1/1 | 1/1 | 1/1
Smallest Ratio | 1 | 1 | 1
Miller İndices (111) |  |  | 
(1,0,0)
(0,1,0)
(0,0,1)
Example-3
1) Determine the intercepts directions
2) Take the reciprocals of the intercepts
3) If fractions result, multiply

## Slide 22
Axis | X | Y | Z
Intercept points | 1/2 | 1 | ∞
Reciprocals | 1/(½) | 1/1 | 1/ ∞
Smallest Ratio | 2 | 1 | 0
Miller İndices (210) |  |  | 
(1/2, 0, 0)
(0,1,0)
Example-4
1) Determine the intercepts directions
2) Take the reciprocals of the intercepts
3) If fractions result, multiply

## Slide 23
Axis | a | b | c
Intercept points | 1 | ∞ | ½
Reciprocals | 1/1 | 1/ ∞ | 1/(½)
Smallest Ratio | 1 | 0 | 2
Miller İndices (102) |  |  | 
Group: Example-5
Can always shift the plane
(note doesn’t make a difference)
1) Determine the intercepts directions
2) Take the reciprocals of the intercepts
3) If fractions result, multiply
Notes: Got to this slide in 50 minute lecture

## Slide 24
Axis | a | b | c
Intercept points | -1 | ∞ | ½
Reciprocals | 1/-1 | 1/ ∞ | 1/(½)
Smallest Ratio | -1 | 0 | 2
Miller İndices (102) |  |  | 
Group: Example-6
Yes, I know it’s difficult to visualize. That’s actually part of the point of doing this one.
(102)

## Slide 25: What are the Miller Indices (h k l) of this plane and the direction perpendicular to it?
Reciprocal numbers are:
Plane intercepts axes at
Indices of the plane (Miller): (2 3 3)
Indices of the direction: [2 3 3]
3
2
2
[2 3 3]
Miller indices are still used for a non-cubic system (even if angles are not at 90 degrees)